# Sunroof Rebuild

Model & year: 91-97 8-Series, U.S. Expertise level: Beginner > Intermediate > Advanced Date: November, 2009 Estimated time to complete: varies (2-3 weeks)

## Tools Required (varies)

- T-25 and T-15 torx

- metal working tools (grinding tips, sandpaper, etc.)

- paint (including factory touch-up)

- other basic hand tools

## Facilities Needed

- Work bench

- Garage (for dry, secure storage)

## Parts Required (varies)

- Toothed Rack (L/R), p/n 54138108869/70, $12.20 list (each)

- Gate Arm (L/R), p/n 54121940965/6, $41.74 list (each)

- Slide Rail (L/R), p/n 54138108887/8, $27.49 list (each)

- Seal Gasket, p/n 54128108334, $94.36 list

Optional

- Sunroof Panel, p/n 54128152848, $331.26 list

- Professional paint match for panel, $200-$300

## Getting Started

Does your sunroof have rust spots? Does it make clunking noises or drag when operating? All of the above? It's rebuild time.

Rust. The 8-series' sunroof panel (#2, diagram 1) is strangely different from other BMW's, constructed of two metal sheets mated together with the assistance of staple joints every 4-5 inches along the outer rim. A formed U-shaped gasket (#5, diagram 1) attaches to the panel instead of the roof itself like other BMW's, which deteriorates over time and traps water at the bottom. When the water soaks the staple joints, rust develops. This explains why rust is typically found every 4-5 inches along the edge. There are two possible solutions:

1) New panel/professional paint match/new gasket - (recommended) this path instantly eliminates all rust but is quite expensive. Complicating this is the adhesive trim on the panel's underside (#6, diagram 1) - another 8-series oddity. It's outrageously expensive to replace (list $693.39). It needs to be re-used or duplicated by an auto upholstery shop in order to keep the price reasonable.

2) Treat rust/new gasket - much more affordable but rust may return (depends on quality of repair). As a DIY, this method is very time consuming requiring light metal work and painting. And even the best DIY spot paint repairs will be noticeable (versus complete re-paint).

Clunking/Dragging. These problems are all related to the sliding ceiling liner (#7, diagram 1). The plastic toothed racks (#12, diagram 2) which control its movement can fail causing uneven tracking. And the gear teeth of the metal slide rail can wear (#21, diagram 2) causing gear slippage. Even the sunroof panel's main lifting gate arms may crack (#14, diagram 2) potentially causing alignment issues. The only repair is parts replacement. See "Frankie's Sunroof Rebuild Kit" above.

Clunking noises can be due to the ceiling liner hitting the rear of the support frame (#1, diagram 2). The liner itself has a flexible perimeter that may be molded for proper fit, to alleviate not just this problem but also help it move with less resistance in the metal slide rail. Liner removal is required.

You will not know the extent of the problem - or the parts to order - until you remove the sunroof and ceiling liner (see procedures below). This is a good project to pair with a headliner replacement, if applicable. However it is not necessary to remove the headliner for this work.

NOTE: your car will be unusable for the duration of the repair (unless you don't mind driving with a missing sunroof). The replacement parts specified above are typically not stocked by dealers and will have to be ordered, delaying any repair. If refinishing the panel, allow for metal work and paint time. If buying a new panel, you could wait until it's painted and ready. Overall, this could mean 2-3 weeks.

## Procedure

Sunroof Panel Removal:

1) Tilt sunroof by pressing up on switch.

2) Reach into partially retracted ceiling liner near the outer edges and feel for the liner's metal release rods. Press gently outboard to release ceiling liner from pin. See image below (panel removed for clarity). Push liner fully rearward.

3) Using T-25 torx, remove the three now-visible sunroof panel screws on inside of each lifting gate arm. Lift panel out; set aside.

4a) You may now begin taking inventory of replacement parts needed. Begin by inspecting the plastic toothed racks for breakage. See image below (racks & covers removed for clarity):

4b) Then inspect lifting gate arms for cracks. See image below (arms removed for clarity).

Ceiling Panel Removal:

5) Remove toothed racks by pulling up on outer edge (to clear cable trolley gear) while pushing rearward. Slide rack off rear of cable trolley while pulling out lock pin. See image below:

6) Slide loose ceiling liner fully forward from "tilt" position. Then fully "open" sunroof (stay clear of moving parts).

7) Slide liner rearward to clear slide rail slot, then pull forward while lifting. Remove liner.

NOTE: DO NOT operate sunroof with toothed racks in place and ceiling liner removed (the toothed racks will snag and break on support frame - ask me how I know). DO NOT allow rain gutter to completely "run over" loose ceiling liner. Keep liner in front of rain gutter when operating motor.

8) Return sunroof to "closed" position. Lift up on inside edge of trolley and attempt to turn gear firmly by hand. Any gear slippage means slide rail needs replacement. (Look also for metal shavings on teeth at rear.) Replace slide rails by removing the five T-15 torx screws with sunroof in full "open" position. Note screw lengths and positions.

9) Remove old gasket seal from sunroof panel. Don't be surprised if water drains as you remove seal. And don't be fooled by rust-colored gasket sealant used by the factory - sunroof rust should be limited to staple joint area. Assess rust damage carefully.

10) At this point you should have enough information regarding replacement parts needed. Order parts. Decide which sunroof panel repair suits your time/budget/skills. Installation is reverse of removal, noting the following:

a) Lift Gate Arms - Detach rain gutter and remove from cable trolley pin by drilling hole into old arm's slide track with hand drill. Install new arms using slip joint pliers for leverage. For better access, remove slide rail to free cable trolley. Verify gate arm slide tracks and wind deflector tab.

b) Ceiling Liner - Inspect ceiling liner for damage. Verify liner pins align correctly with slots from toothed racks. Re-align pins as necessary by tapping with small hammer. See image below:

With sunroof mechanism in full open position, test for freedom of movement BEFORE installing toothed racks. Verify liner moves into slide rail slot when closing. Liner has flexible edges which can be shaped to conform with curvature of frame. Front corners may need to be turned downward in order to catch slot.

c) Toothed Racks - With sunroof mechanism in "closed" position, install racks as shown below.

Once installed, detach rain gutter from lift gates by pressing outward on metal arms and pull rain gutter forward, clear of roof. Install ceiling liner between rain gutter and cable trolley, then slide liner forward to engage racks. Re-attach rain gutter and test liner movement.

d) Sunroof Panel - Apply a small bead of silicone to bottom lip of panel before installing new gasket seal. The seal length is oversize. Trim seal carefully with sharp wire cutters about 1/8" past joint and press into position. Then install panel flush with roof before fully tightening the six torx screws.

e) Sunroof Motor - Remove sunroof switch panel and observe motor while operating sunroof. If motor shifts from torque of drive gear, tighten the T-25 torx mounting screws.

Whew! You're done. Pour yourself a beer and enjoy smooth sunroof operation!

Please leave feedback in my guestbook!

Frankie
Austin, TX